## Slide 1
08/19/2025
Ethan Cao
Shear Flow Modeling

## Slide 2: Agenda
Motivating Example
Modeling Objectives
Data Overview
Model Architecture & Output
Future Steps

## Slide 3: Motivating Example
The concept of shear flow and how it motivates the use of deep learning simulation

## Slide 4: What is a Shear Flow?
Definition: adjacent fluid layers moving parallel to each other with different speeds.
Scenario on the right:
Flow carrying tracer downstream through advection
Tracer spreads and blurs through diffusion
The two fluid layers at the side of the 'white stream' moves at different velocity, hence stretches the tracer

## Slide 5: What is a Shear Flow?
Viscosity: measure of a fluid's internal resistance to a flow, can be thought of as thickness
µ
Shear Rate: The rate at which the fluid is deformed (or difference in velocity) due to shear stress
du/dy
Shear Stress: force per unit area exerted (parallel) to a surface by a fluid, causing layers to slide past each other.
𝞽 = µ x du/dy
(Shear Stress for fluids)

## Slide 6: Couette Flow – Ideal Example
Upper plate moves at velocity U
Bottom plate at fixed Motion
V max
V = 0
Shear Stress applied to cause deformation of fluid layers
Faster layers pulls slower layers forward:
viscosity creates resistance

## Slide 7: Real-World Shear Flow Fluid Dynamics
Crude oil pipeline:
Scenario: As a fluid moves through a pipe, friction at the pipeline’s walls slows the flow and pressure steadily drops. Especially often with cold, high-viscosity fluids or rough pipes.
Application: Predicting velocity and pressure for different pipeline scenarios, evaluating effectiveness of Drag-Reducing Agents (DRAs)
Advantages: fast and data-driven forecasts
High shear stress required due to friction -> more pump power needed to maintain flow
Pressure falls along the pipeline with accumulating friction -> less throughput

## Slide 8: Real-World Shear Flow Fluid Dynamics (in General)
Scenarios of where Shear Flow occurs:
Industrial pipelines: Oil, gas, and water transportation through pipes
Boundary Layers: Air flowing over airplane wings or car bodies
Natural Environments: ocean currents, river shear zones
Lubrication: Thin oil films in engines and machinery

## Slide 9: Modeling Objectives
To predict tracer, pressure, and velocity fields in the shear flow system

## Slide 10: How it motivates the project?
Shear flows driven by pressure exhibit tightly linked advection, viscous diffusion, and pressure effects across fluid layers.
This project aims to utilize deep learning to:
  Predict complex fluid dynamics in a more time-efficient, data-driven way
  Anticipate transport and flow patterns in biological, environmental, and industrial shear flow systems
  Design better pipelines or industrial fluid systems with the knowledge of shear flow behavior

## Slide 11: What are we predicting with PARC?
Velocity fields:
u(x, y, t) and v(x, y, t) – a vector field consisting of horizontal velocity (carries shear layers), and vertical velocity (carries blob perturbations)
Tracer:
s(x, y, t) – a scalar field carried by the flow, indicating the location and the speed of particle diffusion
Pressure Field:
p(x, y, t) – a scalar field that enforces incompressibility and governs the shear flow system

## Slide 12: Data Overview
Overview of the fields and conditions in the dataset provided for shear flow

## Slide 13
Constants in the dataset
Viscosity µ = 1/Reynolds
Diffusivity D = µ / Schmidt
"How does the combination of edge cases of Re & Sc affect shear flow?"
Parameters | Values | Description
Reynolds | ,, , | Determines the state of the flow (smooth or turbulent)
Schmidt | 0.1, 0.2, 0.5, 1.0, 2.0, 5.0, 10.0 | controls the thickness of the flow, determine how quickly tracer spreads and diffuses
Parameters | Values | Description
Reynolds |  | Determines the state of the flow (smooth or turbulent)
Schmidt | 0.1, 0.2, 0.5, 1.0, 2.0, 5.0, 10.0 | controls the thickness of the flow, determine how quickly tracer spreads and diffuses

## Slide 14
Edge Cases of Reynolds and Schmidt
High Reynolds &
High Schmidt:
Strong Advection, Weak diffusion
Low Reynolds & High Schmidt:
Weak Advection, Weak diffusion
High Reynolds &
Low Schmidt:
Strong Advection, Strong diffusion
Low Reynolds &
Low Schmidt:
Weak Advection, Strong diffusion

## Slide 15: Initial Conditions
Parameter | Values | Description
N_shear | 2, 4 | Number of parallel shear layers
N_blobs | 2, 3, 4, 5 | Number of sinusoidal perturbations per layer, controls how many wave-like 'blobs' appear.
W | 0.25, 0.5, 1.0, 2.0, 4.0 | Width of the 'blobs'
Boundary Condition
Frame structure of the simulation – boundaries with periodic flows moving to all sides of the frame

## Slide 16: Initial Conditions
(n_shear=2, n_blob=2, w=0.25)
Blob width (W)
Num of Blobs (n_blob)
Num of shears (n_shear)
(n_shear=2, n_blob=2, w=4)

## Slide 17: Spatial Down Sampling
Reynolds = 2e-1, Schmidt = 1e4
Notes: Aspect ratio changed in downsampling
Velocity field may be impacted by the downsampling

## Slide 18: Temporal Down Sampling
Reynolds = 2e-1, Schmidt = 1e4
Notes: Ideally lower temporal skips
Reduce batch rize of factor of 4 or 8
Increase temporal resolution
  Similar computation
  But better outcomes

## Slide 19: Trajectory Overview
33 data files in total
10 files with 4 trajectories per file -> Original Test Samples
23 files with 32 trajectories per file -> Original Train Samples
The 10 files are duplicates of the same initial/boundary conditions and constants but with different trajectories

## Slide 20: Train-Test Split Strategy
Re-split dataset based off Schmidt numbers for better optimization

## Slide 21: Re-splitting the dataset
Re-splitting the dataset based off Schmidt constant for interpolation and extrapolation
With the same number of trajectories + unique constant and initial conditions

## Slide 22: Training Process
Re-designing differentiator and the data loader for better training

## Slide 23: Model Building Changes
Adjusted Differentiator to take in Reynolds and Schmidt constants fields and consider their time-derivatives as zeroes
  Ensure model learns the real physical dynamics of shear flow
Extracted Single Trajectories for faster training/validation purposes
Adjusted Integrator to take in velocity fields as state variables to ensure model learns velocity evolving in time

## Slide 24: Model Building Changes
Computed spatial reductions & temporal skips for faster and more time-efficient trainings
  Reduced spatial size of data to 1/3
  Skips 10 – 20 temporal steps
  Does not undermine the training output

## Slide 25: Training Strategies #1
Extract two files {Sc=0.5 & 2.0} for both training and validation
Train on full trajectories and validate on single trajectory samples
Compute validation loss at each epoch, select the model with the lowest loss for final inference
Train two models with different integrators at the same time to evaluate performance

## Slide 26: Training Strategies #2 (Current)
Extract two files {Sc=0.5 & 2.0} for validation and all files for training
Train and validate on single trajectory samples
Compute validation loss at each epoch, select the model with the lowest loss for final inference
Train two models with different integrators at the same time to evaluate performance

## Slide 27: Model Output
Outputs of the model from initial rounds of training

## Slide 28: Euler Model Inference
Evaluating model outputs on Train, Test, and Validation Samples

## Slide 29
Snapshot Inference Output – Euler
Integrator: Euler, inference: train samples
Epochs: 1000, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 30
Rollout Inference Output – Euler
Integrator: Euler, inference: train samples
Epochs: 1000, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 31
Snap Inference Output – Euler
Integrator: Euler, inference: test samples
Epochs: 1000, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 32
Rollout Inference Output – Euler
Integrator: Euler, inference: test samples
Epochs: 1000, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 33
Snapshot Inference Output – Euler
Integrator: Euler, inference: validation samples
Epochs: 1000, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 34
Rollout Inference Output – Euler
Integrator: Euler, inference: validation samples
Epochs: 1000, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 35: Euler Loss Curve

## Slide 36: Euler Loss Curve

## Slide 37: RK4 Model Inference
Evaluating the model outputs on Train, Test, and Validation Samples

## Slide 38
Snapshot Inference Output – RK4
Integrator: RK4, inference: train samples
Epochs: 1000, Batch Size: 40, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 39
Rollout Inference Output – RK4
Integrator: RK4, inference: train samples
Epochs: 1000, Batch Size: 40, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 40
Snapshot Inference Output – RK4
Integrator: RK4, inference: test samples
Epochs: 1000, Batch Size: 40, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 41
Rollout Inference Output – RK4
Integrator: RK4, inference: test samples
Epochs: 1000, Batch Size: 40, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 42
Snapshot Inference Output – RK4
Integrator: RK4, inference: validation samples
Epochs: 1000, Batch Size: 40, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 43
Rollout Inference Output – RK4
Integrator: RK4, inference: validation samples
Epochs: 1000, Batch Size: 40, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 44: RK4 Loss Curve

## Slide 45: RK4 Loss Curve

## Slide 46: Observations
Euler: Quicker training iterations, accurate snapshot predictions, loss is unstable and with mediocre rollout predictions
  Appears to rollout better at 100-200 epochs
RK4: slower training iterations, stabler loss, theoretically less error on rollout prediction, but performs poorly due to compounding errors -> different configuration needed
Both models generally predict well on snapshots + very first timestamp of rollout

## Slide 47: Euler Inference at 100 epochs
Interesting Observation of better performance at earlier stages

## Slide 48
Rollout Inference Output – Euler
Integrator: Euler, inference: train samples
Epochs: 100, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 49
Rollout Inference Output – Euler
Integrator: Euler, inference: test samples
Epochs: 100, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 50
Rollout Inference Output – Euler
Integrator: Euler, inference: validation samples
Epochs: 100, Batch Size: 60, Temporal Skip: 50, Training: 11 files + single trajectories, Validation: 2 files + single trajectories , learning rate: 1e-4

## Slide 51: Future Steps
Further steps to take to optimize the model and evaluate its outputs

## Slide 52: Optimization Results so far
Training time accelerated from 8+ hours per training sample w/ full trajectory -> 6.75 minutes per training sample w/ full trajectory.
Reduced rollout inference MSE on training sample from ~0.12 to ~0.0228 (by ~81%)

## Slide 53: Optimizing Inference Quality
Experiment with a range of parameters & configurations
  Learning rates, temporal skips, number of trajectories, number of training samples, integrators
Once optimized fully, check if test and validation results perform equally as good as training samples.
Evaluate the inference quality with physics-based quantitative physics metrics in the ShearFlow equation.

## Slide 54
Thank You
Notes: Lower batch size – lower than 60 to 5 to 2
- Could explain why loss

## Slide 55: Older Documentation Pages
Previous explorations or slides that reflected poor outputs

## Slide 56: Trajectory Analysis
Based on the information from the header file, we know that there are 4 trajectories for each file – we want to compare these to each other across 3 files (at random)
Min/Max Absolute Difference: For each field, we take the trajectories and compute the min & max absolute difference – smallest and largest of those values are the min & max absolute differences
  Why does this good? – Catches any change, anywhere, tells us how similar or not (min & max) the runs are to each other
    At least 1 identical: min = 0
    Every Pair Diff: min > 0 or max >0
    All the Same: max = 0
Conclusion:
  Within files: we have four independent starting points randomized by tracer blobs – same scenario slightly tweaked
  Amongst files: the files differ in terms of flow regime (different Re & Sc), but the way randomization of the blobs occur does not change

## Slide 57: More recent trainings (broken model)

## Slide 58: Snapshot Inference Output – Euler
Integrator: Euler, inference: train samples
Epochs: 100, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: Euler

## Slide 59: Rollout Inference Output – Euler
Integrator: Euler, inference: train samples
Epochs: 100, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: Euler

## Slide 60: Snapshot Inference Output – Euler
Integrator: Euler, inference: test samples
Epochs: 100, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: Euler

## Slide 61: Rollout Inference Output – Euler
Integrator: Euler, inference: test samples
Epochs: 100, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: Euler

## Slide 62: Loss Curve – Euler (recent)

## Slide 63: Loss Curve – Euler (recent)

## Slide 64: Longer training outputs

## Slide 65: Snapshot Inference Output – Euler
Integrator: Euler, inference: val samples
Epochs: 1000, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: Euler

## Slide 66: Rollout Inference Output – Euler
Integrator: Euler, inference: val samples
Epochs: 1000, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: Euler
Learning rate – experiment for shearflow
Don’t use the word ‘model’ is wrong, but rather wrong configuration
Pressure – normalize to 0 to 1
Make experiments less than 30 min for 500 epochs – aim for rollout not breaking (tracer)

## Slide 67: Loss Curve – Euler (longer)

## Slide 68: Loss Curve – Euler (longer)

## Slide 69: Snap Inference Output – RK4
Integrator: RK4, inference: train samples
Epochs: 100, Batch Size: 40, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: RK4

## Slide 70: Rollout Inference Output – RK4
Integrator: RK4, inference: train samples
Epochs: 100, Batch Size: 40, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: RK4

## Slide 71: Snap Inference Output – RK4
Integrator: RK4, inference: test samples
Epochs: 100, Batch Size: 40, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: RK4

## Slide 72: Rollout Inference Output – RK4
Integrator: RK4, inference: test samples
Epochs: 100, Batch Size: 40, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , learning rate: 1e-5
Notes: RK4

## Slide 73: Loss Curve – RK4 (recent)

## Slide 74: Loss Curve – RK4 (recent)

## Slide 75: Older trainings (broken model)

## Slide 76: Snapshot Inference Output
Integrator: Euler, Epochs: 1000, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , inference: test samples, learning rate: 1e-5
Notes: Normalization for tracer and pressure – range: 0 to 1 or -1 to 1
Highlight the sample that is used for inference

## Slide 77: Rollout Inference Output
Integrator: Euler, Epochs: 1000, Batch Size: 70, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , inference: test samples, learning rate: 1e-5

## Slide 78: Snapshot Inference Output
Integrator: RK4, Epochs: 1000, Batch Size: 20, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , inference: test samples, learning rate: 1e-5
Notes: The min max for pressure doesn’t look right, there could be another file that dominates the larger range of the pressure field, the range should be ranging from 0 to 1 or -1 to 1. Pressure scale out of scale needs to be address.

## Slide 79: Rollout Inference Output
Integrator: RK4, Epochs: 1000, Batch Size: 20, Temporal Skip: 20, Training: 2 files + full trajectories, Validation: 2 files + single trajectories , inference: test samples, learning rate: 1e-5

## Slide 80: Loss Curve – Euler

## Slide 81: Loss Curve – Euler

## Slide 82: Loss Curve – RK4

## Slide 83: Loss Curve – RK4